Yoel Kortick

Finding and Using Valid Sample SFX targets in Aleph 500

Introduction

Often when checking links from Aleph to SFX on a demo server, test server, or even in a “production” library we need to make sure we have sample records which will successfully link to SFX.   This document shows how to find and enter such sample records.

In addition to this series of Aleph – SFX documents it is recommended to see

Section 20.1 “ALEPH – SFX Integration” in the “General” chapter of the version 18 ALEPH systems librarian guide.

Section 4.14 “Adding an SFX Link Button” in the “Web OPAC” chapter of the version 18 ALEPH systems librarian guide.

ONE

Define desired sfx_base_url and sfx_admin_base_url in $alephe_root/aleph_start.  Here is an example:

setenv sfx_base_url           http://il-cleo01:3210/inbal

setenv sfx_admin_base_url     http://il-cleo01:3210/inbal/sfxadmin

setenv sfx_fetch_address      ,Ip=$Z39_HOST,Port=$Z39_SERVER_PORT

setenv sfx_openurl_version    ver-0.1

setenv sfx_issn_routine       00

TWO

Enter the sfx_admin_base_url so that you can see what Journals may be accessed via the sfx_base_url

If your sfx_admin_base_url is http://il-cleo01:3210/inbal/sfxadmin then enter this IP in the browser:

http://il-cleo01:3210/sfxadmin/inbal/sfxctrl.cgi

Enter the sfx_admin_base_url so that you can see what Journals may be accessed via the sfx_base_url

If your sfx_admin_base_url is http://il-cleo01:3210/keren/sfxadmin then enter this IP in the browser:

http://il-cleo01:3210/sfxadmin/keren/sfxctrl.cgi

If your sfx_admin_base_url is different then change the IP accordingly so that it will be structured like the one above.

If your sfx_admin_base_url is http://demo.exlibrisgroup.com:9003/sfxadmin then enter this IP in the browser:

http://demo.exlibrisgroup.com:9003/sfxadmin/sfxctrl.cgi

THREE

Enter the username and password (you can get the username and password from the people in charge of the sfx support to which you are connecting) (admin admin).

FOUR

Click “Targets” under KB Manager

FIVE

Click “P” for “Portfolio” for a target which is Active (has a “Y” in “Active” column).  Here we will click the “P” for target “ADISONLINE”.

If something is not active then on top you can click “Activate All”.

These three levels of the target should be active

SIX

Find a journal which you want to use as an example for the specific target.

Here “High blood pressure & cardiovascular prevention” (ISSN 1120-9879) has service “getAbstract”

Here “Drugs & therapy perspectives” (ISSN 1172-0360) has service “getFullTxt”

Here “InterStat” has service “getFullTxt”

SEVEN

Make sure the desired journal(s) are catalogued in Aleph with correct ISSN and title.

EIGHT

Search for the record in Aleph.  If desired to see the link to SFX via short view and full view then retrieve the record in both short and full view.

Here is “High blood pressure & cardiovascular prevention” in Short View

Clicking the SFX link goes to this URL (this URL is “sent to SFX”)

http://il-cleo01:3210/inbal?sid=ALEPH:USM01&isbn=&issn=1120-9879&date=&volume=&issue=&spage=&aulast=&aufirst=&auinit=&title=High%20blood%20pressure%20%26%20cardiovascular%20prevention%2E&atitle=&__service_type=&pid=DocNumber=000051397,Ip=il-aleph02,Port=9994

(The URL is based on the file $alephe_root/www_f_eng/sfx-record-ver-0.1)

and opens this window:

EIGHT

Here is “High blood pressure & cardiovascular prevention” in Full View

NINE

Clicking the SFX link from the full view goes to the same URL will go to the same window as when clicking from the short view.

TEN

When user above clicked the SFX link from the short tabular view or the full view the following  URL was created:

http://il-cleo01:3210/inbal?sid=ALEPH:USM01&isbn=&issn=1120-9879&date=&volume=&issue=&spage=&aulast=&aufirst=&auinit=&title=High%20blood%20pressure%20%26%20cardiovascular%20prevention%2E&atitle=&__service_type=&pid=DocNumber=000051397,Ip=il-aleph02,Port=9994

The significant parts of this URL are as follows:

- http://il-cleo01:3210/inbal?sid= The sfx_base_url as defined on ALEPH server in $alephe_root/www_server.conf

- ALEPH:USM01  The database type and name of bibliographic library from which the URL is created

- Other parameters after & Bibliographic information

- IP The IP of the ALEPH web OPAC from which the URL is created

- Port The Port of the ALEPH web OPAC from which the URL is created

This window comes from one of the following two html pages in $alephe_root/www_f_eng:

sfx-record-ver-0.1

sfx-record-ver-1.0

The suffix of the html page is dependent on variable sfx_openurl_version  in $alephe_root/aleph_start:

Since Aleph supports two versions of OpenURL for connecting to SFX, a special parameter in the aleph_start file defines which version of OpenURL is currently used by the system.

setenv sfx_openurl_version    ver-0.1

stands for OpenURL version 0.1, and

setenv sfx_openurl_version    ver-1.0

stands for OpenURL version 1.0

When ver-0.1 is defined the file sfx-record-ver-0.1 will be used.

When ver-1.0 is defined the file sfx-record-ver-1.0 will be used.

This page:

Is coming from www_f_eng/sfx-record-ver-0.1 because this is defined in aleph_start:

setenv sfx_openurl_version    ver-0.1