Yoel Kortick

Controlling Which ISBN Aleph Sends to SFX via the Web OPAC

This document contains two sections:

- The actual rep_change (1302 in version 18)

- An actual example

The rep change

We will focus here on part 3 of the rep change. For more information on OpenURL 0.1 and OpenURL 1.0 see the SFX documentation

il-aleph02-18(1) USM01-YOELK>>rep_change 1302

Description: Support for OpenURL 1.0 and IP filtering for SFX services from ALEPH has been enabled.

The WEB OPAC "Full View of Record" page contains a button with a link to SFX services. The ALEPH system decides whether this link will be active or not by analyzing a response from the SFX server to a request sent by ALEPH containing some of the record's BIB data and a list of services.

It should be noted that OpenURL 0.1 is still used when the SFX link is clicked.

The following are several changes and additions concerning the process described above:

1. ALEPH now supports the standard "OpenURL 1.0" for sending requests and receiving responses from SFX.

Note that for "OpenURL 1.0", only the following set of services defined in ALEPH's tab_sfx are supported by the SFX side:

Service name in tab_sfx     Representation in "OpenURL 1.0"

- - - - - - - - - - -                                          - - - - - - - - - -

getFullTxt                  fulltext

getAbstract                 abstract

getReference                citation

getHolding                  holdings

getTOC                      toc

2. For "OpenURL 1.0", the IP address of the client (Z63-CLIENT-ADDRESS) is sent

to SFX to enable filtering of available services.

3. It is now possible to determine which ISBN of a BIB record will be sent to SFX by setting a value to a new environment variable, "sfx_first_isbn".

If it is set to "Y", only the first ISBN (USMARC field "020") of a BIB record will be sent to SFX.

If it is set to "N" (this is the default), the last ISBN will be taken (as before).

Note that the new environment variable affects both "OpenURL 1.0" and

"OpenURL 0.1" and that it is relevant for USMARC only.

To activate the above, see the Implementation Notes.

Implementation Notes:

(a) To send only the first ISBN of a BIB record to SFX:

1. add the following line to $alephe_root/aleph_start:

setenv sfx_first_isbn         Y

2. Run the command "source $alephe_root/aleph_start" or re-login.

3. Restart the web server.

(b) To enable work with SFX via OpenURL 1.0 and support IP address filtering:

1. Ensure that the SFX server with which ALEPH works supports OpenURL 1.0 for requests sent by ALEPH.

2. Add the following line to $alephe_root/aleph_start:

setenv sfx_openurl_1_0        Y

3. Run the command "source $alephe_root/aleph_start" or re-login.

4. Restart the web server.

Example

We have bibliographic record 000061911 which has two ISBN fields:

The first ISBN is 0-87436-581-3.

The second ISBN is 0-585-02469-3

In full view of web OPAC we have the link to SFX.

Currently the value sfx_first_isbn is set to N

il-aleph02-18(1) USM01-YOELK>>grep sfx_first_isbn aleph_start

setenv sfx_first_isbn         N

When we click the SFX link we get a link an open URL with the first ISBN:

Now, we change aleph_start so that the value sfx_first_isbn is set to Y:

il-aleph02-18(1) USM01-YOELK>>grep sfx_first_isbn aleph_start

setenv sfx_first_isbn         Y

When we click the SFX link we get a link an open URL with the second ISBN: